## Slide 1: Addressing EMI challenges for high side switches and motor drivers in body electronics
Clark Kinnaird and Arun Vemuri
Body electronics & lighting

## Slide 2: Abstract
What are all the components (“knobs”) a designer can use to improve EMC performance (especially emissions) in a design, specifically an automotive electric motor application?
  Waveform shaping
  Electrical filtering
  Dithering, synchronization
  Board layout
  Shielding
  Etc.
How does each component affect the EMC performance (in general terms)?
What cost or penalty is associated with each component?

## Slide 3: Agenda
Sources of emissions
CISPR25 LISN model
Signal shape frequency spectra
Filtering
Board design
Shielding
Conclusions

## Slide 4: Sources of emissions: DC motor drives
Brushed DC motor
Brushless DC motor
PWM drive
Charge pumps
Clocks and switching logic
Brushed DC motor radiated emissions
original
added caps, ferrite, etc.

## Slide 5: EMI test circuit model
ECU
LISN

## Slide 6: signal shaping

## Slide 7: Frequency spectra of waveforms – wave shape

## Slide 8: Frequency spectra of waveforms – duty cycle

## Slide 9: Switching slew rate control
PWM operation – repetitive high-current transitions
Slew rate (rise/fall time) controlled by gate drive current level
Effect of reduced slew rate
  high-frequency harmonics
  reduced power efficiency & thermal impact

## Slide 10: Effect of gate current in time domain
IGATE = 250 mA
trise = 18 ns
IGATE = 70 mA
trise = 92 ns
IGATE = 10 mA
trise = 560 ns

## Slide 11: Effect of gate current in frequency domain
Change the rise time of PWM edges at 20 kHz
Reduced emissions at > 10 MHz frequencies
62 mA gate drive ½ mA gate drive

## Slide 12: Effect of gate current in frequency domain
Chart: 
Chart: 

## Slide 13: Quiz question 1:
A recent (2019) study in the Czech Republic found that broadband radio frequency electromagnetic radiation can:
  Slow down the internal body clocks (circadian rhythms) of cockroaches
  Increase the appetite of small birds, but only the females
  Promote the growth of mold on wet surfaces
  Enhance the taste of citrus fruit

## Slide 14: Polling question 1:
During this pandemic, about how many hours per day are you spending on phone calls for work?
Less than 2 hours
2 to 4 hours
4 to 6 hours
24 hours!

## Slide 15: Spread spectrum & dithering
Clocks
Power supplies
Motor drive
Notes: The basic principle behind spread spectrum is to reduce the effect of EMI by converting a narrowband signal into a wideband signal, which will spread energy across multiple frequencies. For a switching regulator, this can be done by manipulating the oscillator that sets the switching frequency, and can be done for most switch mode power supply topologies (buck, boost, and so forth). Conservation of energy requires the total energy to remain constant, but by spreading this energy across multiple frequency bands, peak energy is minimized. As a result, nearby sensitive circuits (hereafter referred to as victims) will be less perturbed by the interference. Figure 1 illustrates how manipulating the clock frequency over time has the effect of spreading energy generated by a switcher.

## Slide 16: Integrated FET high side switch - dithering
Dithering or spread spectrum reduces the peak amplitude of periodic signals.
This example is TPS1HB04-Q1

## Slide 17: Filters
Power
Switching
Stage

## Slide 18: Pi filter reduces PWM pulses
Attenuates differential-mode noise
Effective for low frequencies

## Slide 19: Common mode filter (choke)
Attenuates common-mode noise
Effective for high frequencies
https://e2e.ti.com/support/sensors/f/1023/t/570116

## Slide 20: Decoupling capacitors
Decoupling capacitors should be distributed across the entire board to help reduce the board resonances. These board resonances are the main decoupling problem at high frequencies (above about 20 MHz). The actual resonant frequency will change as the number, or location, or value of decoupling capacitors is changed.
Traditional values of capacitance (for example, .01 uF) make a significant improvement in frequencies below about 200 MHz, but make only a little change at higher frequencies. This is mostly due to the self resonance of the capacitor, and the inductive nature of the capacitor above its natural resonant frequency. Therefore, high frequency capacitors should also be distributed across the board. The value of these capacitors will determine the frequency range over which they are effective.
https://e2e.ti.com/blogs_/archives/b/precisionhub/archive/2013/08/13/the-decoupling-capacitor-is-it-really-necessary

## Slide 21: shielding

## Slide 22: Shielding
Shielded components
Shielded board
Shielded cables
Source: MWFR.com

## Slide 23: Emission reduction at the motor
Source: Maxon Group
Use a brushless motor.
Install suppression capacitors between the terminals and the ground shield.
Install a toroidal ferrite core on the motor leads.
Pair motor leads and shield, if possible.
Controllers with a linear power stage produce less emissions on the motor lines than controllers with PWM actuation of the motor.
Encapsulate the motor in a grounded housing (the principle of a Faraday cage).

## Slide 24: Shielded and unshielded inductors
Source: Wurth Elektronik

## Slide 25: Twisted pair and untwisted motor wires
Radiated emissions from 40 MHz to 1 GHz
Variable gate drive current, 10 mA to 500 mA

## Slide 26: Quiz question 2:
A paper published by the American Institute of Physics this year documented how Chinese scientists used Maxwell’s equations and finite element analysis to determine:
  Whether a kettle or microwave is the best way to heat water to make tea
  Optimal charging rates for 5G smart phones in sub-ocean caves
  How 14-year olds send such a high number of texts per minute
  Which is better for coding, using spaces or tabs

## Slide 27: Polling question 2:
Which sport do you most enjoy watching?
Soccer/football
Cricket
Tennis
Wrestling
Badminton
Auto racing
Kabaddi
Hockey
Cycling

## Slide 28: board layout

## Slide 29: Board layout – critical loops
Small loop size
Separate from other signals

## Slide 30: Board layout
Grounding
Board layers

## Slide 31: Layout suggestions
Minimize crosstalk due to capacitive coupling by increasing the separation between tracks.
Place the power and ground in parallel to maximize the PCB capacitance.
Place sensitive and high frequency traces away from high noise power traces.
Widen ground and power traces to reduce the impedance.
Divide the circuit into functional sub-circuits to keep return currents as close as possible to the sources.
Connect decoupling capacitors between power and ground at each chip, as close as possible to the pins. This helps to filter out switching transients.
Avoid right-angle corners in traces; make to 45 degree angles instead.
Keep trace widths constant and avoids stubs in the traces.

## Slide 32: Connection of decoupling capacitors

## Slide 33: conclusions

## Slide 34: Conclusions
Each application presents different requirements and may require different combinations of individual EMI mitigation techniques
Reducing the source of emissions can be accomplished with wave shaping, dithering and spread spectrum techniques.
Filtering primarily reduces conducted emissions
Shielding primarily reduces radiated emissions
Board layout is important to reduce both conducted and radiated emissions
Best practices are documented in numerous TI application notes

## Slide 35: Sources and further reading
Input Filter Design for Switching Power Supplies, TI application report SNVA538, 2010, https://www.ti.com/lit/pdf/snva538
Reduce buck-converter EMI and voltage stress by minimizing inductive parasitics, TI Analog Applications Journal, Fall 2016, https://www.ti.com/lit/an/slyt682/slyt682.pdf
Reduce Conducted EMI in Automotive Buck Converter Applications, TI Application Report SNVA886, July 2019, https://www.ti.com/lit/an/snva886/snva886.pdf
EMI filter components and their nonidealities for automotive DC/DC regulators, https://www.ti.com/lit/an/slyt782/slyt782.pdf
EMI Reduction Technique, Dual Random Spread Spectrum, TI application report SNVA874, June 2020, https://www.ti.com/lit/an/snva974/snva974.pdf
Passing CISPR25-Radiated Emissions Using TPS54160-Q1, SLVA629A–December 2013–Revised May 2019, https://www.ti.com/lit/an/slva629a/slva629a.pdf
PCB Design Guidelines For Reduced EMI, https://www.ti.com/lit/an/szza009/szza009.pdf
EMI/RFI Board Design, May 2004, https://www.ti.com/lit/an/snla016b/snla016b.pdf
Printed Circuit Board Decoupling Capacitor Performance For Optimum EMC Design - Bruce Archambeault,, Doug White, Electromagnetic Compatibility Center of Competency, January 1999, https://studfile.net/preview/429206/
Bypass Capacitor Sequencing, High-Speed Digital Design Online Newsletter: Vol. 9 Issue 07, http://www.sigcon.com/Pubs/news/9_07.htm
Brushed DC Motor – EMC Radiated Emissions Problems and Improvements 18th July 2017 in Recent Work by James Pawson, https://www.unit3compliance.co.uk/brushed-dc-motor-radiated-emissions-improvements/
Near Field Scanners Let You See EMI, EE News Embedded, https://www.eenewsembedded.com/news/near-field-scanners-let-you-see-emi