## Slide 1: Multiplying DAC Essentials
A deep dive into Multiplying DACs and Applications
Notes: Hello, my name is Kevin Duke and I am an analog applications engineer for the precision DAC group. Thanks for joining us for this deep dive session.

## Slide 2: Agenda
What is an MDAC?
  Other DAC Architectures
    String DAC
    R2R DAC
  Multiplying DAC (MDAC)
MDAC Circuits and Analysis
  Two-Quadrant and Four-Quadrant Configurations
  +/-10V 4-Quadrant MDAC TI Precision Design
    Selecting the output amplifier
MDAC Applications
  AC Signal Generation
  AC Attenuator
  DC Load Module
  20mA Source/Sink
Notes: Today we’re going to focus on the MDAC precision DAC architecture. We’ll begin by looking at the other architectures and explaining why the MDAC is an attractive option, followed by a deep dive on building 2-quadrant and 4-quadrant MDAC circuits, and finally we’ll cover some applications we see MDACs used in.

## Slide 3: What is an MDAC?
Notes: 3
The first question to answer is what makes a multiplying DAC any different than the other kinds of DACs? After-all, the output for any DAC is simply the reference voltage multiplied by a ratio of the input code to the device’s resolution.
Lets look at all of the precision DAC architectures to answer this...

## Slide 4: String DAC
One resistor/switch pair for each code
Large number of resistors (2bits)
Trimming 2bits resistors is impractical, strong linearity requires good IC layout
The input impedance for the reference node can be high with the series resistor string
  Usually string DACs are low power
  This may lead to higher noise
Interpolating amplifier can be used to reduce the number of resistors and reduce package size
Simple to design – low cost
Full-scale Output
Zero-Scale Output
Notes: The string DAC is the most straight forward precision DAC architecture. It is simply a collection of resistors in series with a tap node between each of the resistors. When a digital input code is applied to the DAC it is decoded and the output switches move to the appropriate configuration. For instance, (CLICK) when a full-scale code is applied the top-most switch closes and the output goes to full-scale. (CLICK) When a zero-scale code is applied the bottom-most switch is closed, and the output goes to at zero-scale. (CLICK)
Ideally, every resistor down the chain creates a voltage drop equal to one LSB. In a straight forward string DAC design, there is one resistor/switch pair for every code that can be applied to the DAC. (CLICK) Because of this, as resolution increases the number of resistors and switches in the string DAC design exponentially increase. (CLICK)
Since trimming 2^(number of bits) resistors to match one another is not very practical, delivering good DNL and INL performance from a string DAC is heavily dependent on good IC layout. Generally speaking, string DACs have the worst linearity of all precision DAC architectures. (CLICK)
The input impedance for the reference node is usually high-impedance due to the volume of resistors in the string. This makes most string DACs low power devices, but it comes at the sacrifice of increased noise at the DAC output. (CLICK)
An interpolating amplifier is typically used for the output buffer to reduce the number of resistors required in the design and keep the package size small. Without the interpolating amplifier even medium resolution string DACs would probably come in impractically large packages. (CLICK)
Finally, the simplicity of the string DAC design and non-existent, or very limited, trim process delivers the lowest cost precision DAC option.

## Slide 5: R-2R DAC
Each switch is one bit of the DAC resolution
Major carry glitch energy can be substantial
Few resistors allows trim to deliver high linearity
Switch Closes
312.5mV
Switch Closes
625mV
Switch Closes
1.25V
Switch Closes
2.5V
The input impedance of the reference node is code dependent, which increases settling time
Typically lower impedance than the string
  Improved noise performance, more power
Notes: The R-2R ladder is a bit more complex than the string DAC. The R-2R ladder is a binary weighted voltage divider. Each switch and 2R leg, except for the termination 2R leg, represents one bit of the DAC’s resolution. In this example we have a 4-bit R-2R ladder, lets assume a 5 volt reference.
(CLICK) When the left most switch closes the output is equal to one LSB, 312.5mV.
(CLICK) The second switch generates 2 LSBs on the output, 625mV
(CLICK) The third switch generates 4 LSBs, 1.25V
(CLICK) The fourth switch generates 8 LSBs, or midscale, 2.5V
(CLICK) We’ve shown that each switch is one bit of the DACs resolution. This helped reduce the number of resistors from 2^(number of bits) down to 2 times the number of bits. When the input code to the DAC only causes one bit to change the glitch energy is minimal, similar to a string DAC. However, when the input code causes multiple bits to change several switches must move (CLICK) and the output glitch energy can be substantial. This is referred to as a major carry transition.
Increased glitch energy is a trade-off we have to live with for reducing the number of resistors in the design. (CLICK) The benefit, though, is that a comprehensive trimming scheme can be implemented on each of the resistors to deliver superior linearity.
(CLICK) Unlike the string DAC, the R-2R DAC reference input impedance is code dependent which can increase settling time. (CLICK) This impedance is typically lower than that of the string DAC and while that may increase power consumption, it also can also decrease noise on the DAC output.

## Slide 6: Multiplying DAC (MDAC)
Reference input and DAC output have swapped
Reference input impedance is static
  Settling time has improved over R-2R DAC
Output amplifier is not included on silicon
  External transimpedance stage is required to get a voltage output
  Switches move from GND and virtual GND – reduced glitch
Notes: The R-2R DAC made several improvements over the string DAC, but still had its flaws. Linearity and noise performance were improved but at the cost of increased glitch energy and increased settling time. The multiplying DAC addresses these issues.
The MDAC utilizes the same R-2R ladder that the R-2R DAC used, but with some differences. (CLICK) The biggest difference is that the reference input and DAC output have swapped. This results in the MDAC R-2R ladder creating a binary weighted current divider, while the R-2R DAC was a voltage divider. Subsequently, the output of a MDAC is a current, not a voltage.
(CLICK) Another effect of this swap, is that the reference input impedance is now static. Since the reference load is static the reference drive does not have to settle in addition to the output amplifier during a code change, which allows the MDAC to exhibit better settling time than the R-2R DAC.
(CLICK) As shown in this diagram, an external amplifier in a transimpedance configuration is required to convert the MDAC current output into a voltage. The requirement of an external amplifier to get a voltage may seem like a drawback for a MDAC at first, but it actually provides a great deal of flexibility and allows customers to tailor the performance of their DAC system to their needs.
Typically precision DACs are produced on the HPA07 process for its density. Precision op amps, on the other hand, are produced on a variety of other processes that are better for pure analog performance. The MDAC allows the combination of the best of both processes without having to produce an expensive, low-yield, MCM solution.
Finally, the external amplifier forces the current output terminal of the MDAC to 0V. This means the DAC switches will typically be moving between GND and virtural GND, which reduces glitch energy.
All of these elements, especially it’s static input impedance and lack of a reference input buffer or output buffer, help the MDAC function as a good medium frequency AC attenuator – we’ll look at this in a little more detail later. This unique functionality is what earns the MDAC it’s namesake.

## Slide 7: MDAC I – V Conversion
5mA
2.5mA
1.25mA
625uA
1.25mA
625uA
312.5uA
312.5uA
2.5mA
0
1
0
1
MSB
LSB
3.125mA
0A
3.125mA
3.125mA
-3.125V
Notes: Lets step through a complete example, from reference input to transimpedance output, of a typical MDAC setup. For this example we’ll assume a reference voltage of 5V, R = 1k ohm, 2R = 2k ohm, and Rfb = 1k ohm. Since both ends of all of the DAC switches are terminated to GND, we can see that the parallel equivalent resistance of the R-2R ladder is 1k ohm, (CLICK) so the current flowing into the reference terminal is 5mA.
At the first node, and each subsequent node, this 5mA current will see a 1/2 current divider between equivalent impedances of 2R and 2R. So the first node will send (CLICK) 2.5mA down it’s R-2R leg, (CLICK) 1.25mA down the second, (CLICK) 625uA down the third, and (CLICK) 312.5uA down the fourth.
Lets suppose that code 0101 is written to this DAC (CLICK). The current from legs one and three will be sum to 3.125mA at the Iout terminal. (CLICK) For now, we’ll assume an ideal op amp at the output so that no current flows into the inverting terminal. Instead, all of the current will flow across the 1k ohm feedback resistor. This creates 3.125V at the inverting terminal of the op amp, in order to keep the inverting and non-inverting terminals equal (CLICK) the op amp will create an equal and opposite current across the feedback resistor. In order to do this, the op amp must output -3.125V .
(CLICK) Here’s the complete transfer function for the MDAC + Amplifier combination. Notice that the polarity of the output voltage is inverted compared to the reference input.

## Slide 8: DC MDAC Circuits and Analysis
Notes: 8
Next we’ll move to DC MDAC circuits and some circuit analysis

## Slide 9: Two-Quadrant and Four-Quadrant MDACs
Notes: There are two primary configurations for an MDAC: two-quadrant and four-quadrant.
In a two-quadrant configuration the polarity of the output is controlled by the reference swinging either positive or negative. The DAC code cannot cause the output to change polarity. The DAC code only controls the magnitude of the DAC output.
With a negative reference input, increasing the DAC code causes the output voltage to increase, from 0 to positive Vref.
With a positive reference input, increasing the DAC code causes the output voltage to decrease, from 0 to negative Vref.
(CLICK)
In a four-quadrant configuration the polarity of the output can be controlled by the reference swinging positive or negative. Additionally, the DAC code can also change the polarity of the output.
With a negative reference input, increasing the DAC code from zero to full-scale causes the output to swing from negative Vref positive Vref.
With a positive reference input, increasing the DAC code from zero to full-scale causes the output to swing from positive Vref to negative Vref.
In most uses the reference input is not moving, so in general, two-quadrant configurations can be thought of as unipolar and four-quadrant configurations can be thought of as bipolar.

## Slide 10: Simple Two-Quadrant Designs
Notes: Now we’ll look at some simple two-quadrant MDAC circuits with static reference inputs.
With this basic circuit, we have a positive reference source with a single supply buffer driving the MDAC reference input. The output is the standard transimpedance stage and the output voltage is negative. In most applications, an inverted output with respect to the reference is not desired.
(CLICK) The most straightforward solution to this polarity problem is to add an inverting amplifier stage to the output. The downside of course is that we had to buy another op amp and two resistors. The tolerance of the resistors and the performance of the additional op amp will degrade system performance.
(CLICK) An alternative is to move the inverting stage to the reference input. We already had a reference buffer in the original schematic, so all we had to add to get a positive output voltage was two resistors. The resistor tolerances still have an impact on this system and will degrade performance.
(CLICK) This design gets around adding another op amp and adding any additional components. In this circuit the reference source GND is connected to the output of an op amp. The reference output voltage is applied to the inverting input terminal of the op amp and the op amp non-inverting terminal is connected to GND. In order to drive the inverting input to GND the op amp will drive the reference source’s GND pin to negative REFOUT, causing 0V to appear at the inverting input.
This solution has it’s limitations and may not fit in all systems, but when applicable this is the most accurate solution.
Any of these circuits are considered two-quadrant MDAC configurations.

## Slide 11: Simple Four-Quadrant Design
Two-Quadrant Circuit
Summing Stage
Notes: The typical four-quadrant design is comprised of (CLICK) the same basic two-quadrant circuit we looked at on the previous slide (CLICK) followed by a summing amplifier stage to provide gain and offset.
When RG2 and RFB2 are equal and RG1 is half of RG2 the output swings symmetrically about the reference. In this case it’s usually not as desirable to do anything to invert the reference input. With a positive reference in this circuit the output swings from negative Vref to positive Vref as the DAC code is increased, which is the most intuitive configuration for most applications.
This circuit does depend on resistor tolerances to have success, but there isn’t any work around for this issue. Some devices, however, do provide these resistors on silicon – such as the DAC8822, which can ease the burden of purchasing high tolerance resistors.

## Slide 12: ±10V 4-Quadrant MDAC TI Precision Design
Both 2-quadrant and 4-quadrant designs require a transimpedance stage
  4-quad is just 2-quad with a summing amp
How do you select the amplifier for this transimpedance stage?
  Most MDAC datasheets show this:
Notes: Regardless of if you’re designing a two-quadrant or four-quadrant MDAC circuit, you need a transimpedance stage to convert the DAC output into a voltage, but what parameters are important for selecting this amplifier?
In most MDAC datasheets across the industry, you’ll find something in the theory of operation section that looks like this (CLICK). This excerpt from the DAC8811 datasheet says that the external transimpedance amplifier must have sufficiently low input offset voltage such that the amplifier offset is not modulated by MDAC Iout impedance changes. This effect means that amplifiers with large input offset voltage can produce INL errors.
So we know we need to get an amplifier with low Vos, but how low? And, are there any other specificaitons we should care about? (CLICK) To answer these questions we created a TI Design about designing a +/-10V 4-Quadrant MDAC circuit. Remember that a 4-quadrant circuit is just a 2-quadrant circuit with an additional summing stage, so this document also can help design 2-quadrant circuits.
Before we jump into the TI Design, lets look at what happens when an MDAC is paired with an amplifier with large input offset voltage in a simple TINA-TI simulation.

## Slide 13: Simple TINA-TI Simulation
Input Code | Vout | LSB Size
00 | 0V | *
01 | -1.25V | -1.25V
10 | -2.5V | -1.25V
11 | -3.75 | -1.25V
Input Code | Vout | LSB Size
00 | -1V | *
01 | -2.625 | -1.625V
10 | -4.000 | -1.375V
11 | -5.625 | -1.625V
Vout with 1V Vos
Vout with 0V Vos
Notes: In this simple example we have a 2-bit MDAC in a two-quadrant configuration. The output codes step from 0 to -3.75V and the LSB sizes between each step are all the same and equal to -1.25V. It is perfectly linear.
(CLICK) If a 1V battery is added between GND and the non-inverting terminal of the op amp we can simulate an amplifier with excessive input offset voltage. In this case we see the output step from -1V to -5.625V. We certainly expected to see the output range skewed by the input offset voltage of the transimpedance amplifier, but we also see that the LSB step size between each code changes. This system is non-linear due to the input offset voltage of the transimpedance amplifier being modulated by the MDAC Iout impedance.
This is simple to digest for a 2-bit MDAC, but what about for a more realistic 16-bit MDAC? What if that MDAC also has segmentation implemented? In these cases it isn’t as trivial to determine the impact of the amplifiers input offset voltage, especially if the amplifier has a more realistic input offset voltage spec.

## Slide 14: How to Analyze Modulation on Vos
Four-Step Process
  Analyze the R-2R ladder structure
  Write nodal equations for each “rung” of the Ladder
  Define Iout impedance versus code
  Iterate through all possible codes
Notes: The figure here models the Iout input impedance with the resistor Ros. As Ros changes and Rfb stays constant the input offset voltage of A1 is modulated.
To analyze this modulation we need to be able to estimate the value of Ros. We can use a four-step process to get there.
First, look at the R-2R ladder architecture. Most modern DACs have some simple segmentation scheme to help deliver strong linearity.
For the given R-2R ladder structure, nodal equations must be written to describe the voltage at each rung of the R-2R ladder.
With the nodal equations the Iout output impedance can be derived and iterated through with software to determine the point where the the amplifier contributes the greatest INL error.
It should be noted that this process provides a reasonable estimate of the effects of Vos on linearity. This does not take complex trimming schemes into account to be absolutely accurate.

## Slide 15: Example R-2R Ladder Architecture
Notes: We’ll use a simple example of a 5-bit R-2R ladder with the 2 MSBs segmented. The techniques used to analyze this ladder can be extended to any other MDAC architecture with a similar segmentation scheme. Most TI MDACs follow this scheme or something very similar.

## Slide 16: Nodal Equations
General Form Equations
n: number of non-segmented bits i: bitnumber
Notes: For modeling the input impedance of the R-2R ladder the reference voltage is replaced by GND. In this case the nodal equations for the segmented legs would simply be the voltage present at the Iout terminal divided by R or 2R for B1 and B2 respectively.
The input impedance for the non-segmented legs can be modeled by the circuit on the screen. We have voltages noted at the top of each rung of the R-2R, V2 through V5.
In this model V2 is simply GND and does not need a nodal equation. The rest of the equations can be derived with simple circuit analysis. The tricks to this step are that we have added boolean variables, values that are constrained to either 0 or 1, to the equations to represent the binary input code and switch movement. Additionally the resistor values have been normalized to the value R.
We’ll keep the V2 variable around in the V3 equations to help us develop general form equations to use for other DACs shown here (CLICK)
In these general form equations s is the number of segmented bits, I is the node or bit number, and n is the total number of bits. The first equation applies to all non-segmented bits except for the MSB. The second equation applies to the terminated LSB.

## Slide 17: Define Iout Input Impedance
Notes: To simplify modeling the Iout input impedance we’ll rearrange these three equations to be defined in terms of bits only, rather than bits and voltages. (CLICK)
These simplified equations will be used to iterate through all of the bit combinations. The last thing we need to do before we get there is define the current through each of the five rungs of the ladder and calculate input impedance. (CLICK) The simplified nodal voltages are used directly in these current equations.
Remember that the leading boolean values in each equation are used to model the input code and corresponding switch movement. When a switch is not connected to Iout it’s boolean value will be set to 0 and it will not sum into the Iout current.
The final step will be to calculate the resistance Ros using simple ohms law. That is the voltage at the Iout terminal divided by the current at the Iout terminal due to the DAC input code.

## Slide 18: Define Iout Input Impedance
Notes: The set of equations can be dumped into MATLAB or the program of your choice to iterate through all of the input codes. Here you can see the results for the 5-bit, 2-MSB segmented MDAC. In this case the minimum value of Ros that causes the most gain to the input offset voltage of the transimpedance amplifier occurs at the full-scale code.
In this case the maximum gain on Vos is about 2.1.
It may not come as a surprise that the worst case occurs at full-scale, but that is only a coincidence for this particular MDAC.

## Slide 19: Define Iout Input Impedance
Notes: This set of results are for a real DAC, the DAC8811. This time the maximum gain on the input offset voltage occurs at code 64171, not the full-scale 16 bit value of 65536.
Similar to the previous case though, the maximum gain on Vos is about 2.25. As a general rule of thumb, to avoid doing all of this math, most MDACs worst case INL error caused by Vos of the transimpedance amplifier can me estimated by 2.4*Vos.
All of the MATLAB code used to generate these curves will be included in the +/-10V 4-Quadrant MDAC TI Precision Design design archive when this document releases for you to reuse.

## Slide 20: Input Bias Current
Input Code | Vout | LSB Size
00 | 0V | *
01 | -1.25V | -1.25V
10 | -2.5V | -1.25V
11 | -3.75 | -1.25V
Input Code | Vout | LSB Size
00 | 1V | *
01 | -250mV | -1.25V
10 | -1.5V | -1.25V
11 | -2.75V | -1.25V
Vout with 1mA Ib
Vout with 0A Ib
Notes: An additional parameter of the output amplifier that will impact system performance is input bias current. Input bias current directly leeches or adds current to the MDAC output current that will create an offset term across the transfer function of the DAC.
To show this we’ll again use a simple TINA-TI simulation. We start with the basic 2-bit DAC example and step across all of the codes. This time an ammeter is placed in series with Iout to show the current flowing into the transimpedance stage. (CLICK)
If a current source is placed to drain current from the the op amps inverting terminal to GND we can simulate input bias current. In this example we use 1mA and across all of the DAC output codes we see a constant offset voltage of +1V.
In general, the effects of input bias current can be modeled by the equation at the bottom of the screen.

## Slide 21: How to pick the trans-impedance stage amplifier?
Low input offset voltage is important to keep linearity specifications
  Approximate effects of Vos on linearity as: 2.4 * Vos
  Remember that Vos Drift, CMRR, and PSRR can also impact Vos
  Amplifier Vos and MDAC linearity are uncorrelated sources
Low input bias current is important to avoid introducing an offset voltage
  On their own MDACs do not have an offset error specification
TUE Equation:
Notes: In summary, low input offset voltage is important to maintain good linearity. How low the input offset voltage needs to be is dependent on the linearity and total error goals for the system. Remember that amplifier Vos and MDAC INL are uncorrelated sources, so the most appropriate method to express total INL is with an RSS technique, not with direct summation.
Low input bias current is also import to keep offset error in check. By itself the MDAC does not have an offset error specification.
To summarize these error sources all of the specifications should be converted to one unit, usually %FSR, and RSS’d together since they’re all uncorrelated sources. For a complete example on all of these calculations, full error analysis including the summing amplifier stage, and collected results – please look at the +/-10V 4-Quadrant MDAC TI Design.

## Slide 22: MDAC Applications
Notes: 22
Now we’ll take a brief look at a few MDAC applications.

## Slide 23: AC Attenuator
AC waveform is fed into VREF
DAC input code sets attenuation
Notes: One of the most unique applications of a multiplying DAC is to control the gain or attenuation of a varying DC signal or an ac signal. This application is most commonly referred to as an AC attenuator.
For most DACs, the reference must be an extremely stable DC voltage. However, in applications like this, the reference input is actually the varying DC signal or AC signal. Attenuation is set by applying a digital code to the DAC. This example graphically illustrates this application where a sinusoid is fed into the reference input and applying different input codes attenuates the signal from
Mid-scale(CLICK)
to quarter-scale (CLICK)
to 1/8th scale (CLICK)
to zero-scale
The MDAC reference can vary significantly in amplitude and frequency. In fact the reference to an MDAC can be substantially greater than the supply voltage itself. For example, the DAC8811 has an analog supply range of 2.7V to 5V. However, the reference input can support up to +/-15V.

## Slide 24: Parasitic Frequency Attenuation
Bandwidth is not the same at all codes.
More attenuation = Less bandwidth
Notes: In most 2-quadrant and 4-quadrant implementations, the output capacitance of the R-2R ladder, the trans-impedance amplifier’s input capacitance, along with other parasitic capacitances introduce a pole into the open-loop response. This can cause ringing or instability when the loop is closed. To compensate for this, an external feedback compensation capacitor (C1 in the figure) is usually connected in parallel with the internal feedback resistor of the MDAC. Since the internal output capacitance of the DAC varies with code, it is difficult to fix a precise value for this capacitor. The datasheet typically includes a recommended value for this compensation capacitor. All this affects the bandwidth of our multiplying function.
The reference multiplying bandwidth is the frequency at which the gain is –3 dB. For a given device, it is a function of amplitude and the choice of compensation capacitance. The figure shown here is taken from the DAC8812 datasheet. It plots the attenuation in dB for various codes over frequency. For example, for an attenuation factor of 6 dB (which is mid-scale or divide by 2), DAC8812 has a flat response up to almost 10 MHz. A consideration here is to choose the bandwidth of the accompanying op amp such that it introduces insignificant dynamic errors.
The TI Design we went through focused on DC performance. For applications where the reference input is a relatively high speed signal, choose a wide-bandwidth, high-slew-rate op amp to avoid distortion. The gain-bandwidth of the trans-impedance circuit is determined by the impedance of the feedback network and the gain configuration. A good rule of thumb is to select an op-amp with a –3 dB bandwidth that is 10 times the frequency of the reference signal.

## Slide 25: AC Waveform Generator
VREF is a constant DC voltage
Fast settling can help generate waveforms
Requires a trans-impedance stage with a high-speed amplifier
Parallel interface is helpful to latch codes to the input faster
Notes: Another related application for MDACs is to generate waveforms using a fixed reference. Because a fast-settling DAC is required to generate ac signals while minimizing distortion, MDACs are a good choice due to their inherent fast settling times. The design of the trans-impedance stage is critical with the need for high-speed amplifiers. In addition, parallel interfaces to load the DAC codes will prevent the digital interface from becoming the limiting factor because a number of codes must be loaded in a short time to generate the full waveform. An example of a TI DAC with a parallel interface is DAC8822.

## Slide 26: DC Load Module
Precision DAC are used to adjust the loading for the module
The I-V converts the current to voltage
This voltage is applied to the MOSFET (gate side) to create dynamic loading
Hence name “DC Load”
Notes: DC load modules require dynamic loading to be created on the DC power supplies that are being tested. This is generated by controlling the gate of a MOSFET which provides the loading current. The precision DAC is paired with a trans-impedance amplifier to control the gate of the MOSFET.
System tests on these power supplies require the current load to change rapidly. This imposes a requirement on the DAC+trans-impedance stage that the voltage generated by this signal chain has an ability to change rapidly. Therefore, a key care-about in this signal chain is a fast settling DAC (usually <1usec). Additionally, in order to accurately control the loading current, a high resolution DAC (>16 bit) is preferred. Some modules also require a periodic signal to create a loading current to the supplies.
All these requirements call for a DAC with high resolution, fast settling time and the ability to attenuate a periodic signal. An MDAC with the right output amplifier can deliver all of these characteristics, and we have seen success in the past in this application space.

## Slide 27: 20mA Source/Sink
Benefits
High Voltage Compliance
Bi-directional current flow
From DAC8811 datasheet:
Notes: Shown here is a modified Howland current pump circuit for Voltage to Current conversion. We will not delve into this circuit because of time constraints but you can refer to the DAC8811 datasheet for more information. Bi-directional current flow and high voltage compliance are two features of this circuit. Sizing capacitor C1 is critical for differential stability.
Given the performance we’ve seen multiplying DACs are capable of, MDACs can find homes in virtually any application that require extremely high precision, including high performance industrial analog output modules or test equipment.

## Slide 28: Closing Information
Notes: 28

## Slide 29: MDACs on www.ti.com
Notes: So how do you find MDACs on www.ti.com? Recently we’ve put a lot of effort into improving the parametric search tool on the precision DAC landing page and have added a few parameters to the search table.
To show all MDAC devices, first navigate on the main www.ti.com web page to the product folder for Precision DAC (=<10MSPS). On that page click on the Add/Hide Parameters tab shown here
(CLICK)
This opens a table where parameters can be added or removed. By adding the “Architecture” parameter to the table, (CLICK)
we get an additional column titled “Architecture” in the table. (CLICK)
Note that we have about 25 parts in our portfolio. Also notice that all these DACs are considered a current output.

## Slide 30
Dual
Quad
Single
DAC8811
SPI
DAC8812
SPI
DAC8814
SPI
DAC8820
Par Input
DAC8822
Par Input
DAC8801
SPI
DAC8806
Par Input
DAC8803
SPI
DAC8802
SPI
DAC8805
Par Input
TI’s Multiplying DACs
12 Bit
14 Bit
16 Bit
DAC7811
SPI Input
DAC7821
Par Input
DAC7822
Par Input
DAC7800
SPI Input
Notes: As we saw, TI has a large portfolio of MDACs ranging from 8 bit to 16 bit with single or multi-channel options and choices of serial and parallel interfaces.
Since, the MDACs are often used for waveform generation and signal attenuation – a parallel interface for the digital input is quite common.
The X-Y charts shown here highlights some of the latest high resolution MDACs from TI.

## Slide 31: 2013 DAC Collateral
Blogs
  9-Part DAC Essentials Series on Analog Wire
TI Precision Designs
  +/-10V From a Unipolar DAC
  +/-10V 4-Quadrant MDAC
  High Voltage, High Current, Programmable Power Supply
“Engineer It” Videos
  What is a MDAC?
  Choosing a Precision DAC
Presentations
  Precision DAC Essentials
  Industrial DAC Essentials
  Designing Industrial Outputs with DAC + XTR Products
Notes: Before we answer any questions you might have, there is additional technical collateral we’d like to bring your attention to that the Precision DAC team has generated this year to help you promote and understand our portfolio. (CLICK)
The “DAC Essentials” series is a blog on Analog wire which has generated a lot of good feedback. It goes through all of the precision DAC basics and culminates in an explaination of total unadjusted error that draws everything together (CLICK)
We have released 2 TI Precision Designs using our catalog DACs, with a third on the way. We discussed one of them today. In addition, we also have a TI Precision design generating a +/-10V output from a uni-polar string DAC and one on generating a 36 V, 1 A SPI controlled power supply with an integrated current shunt monitor. (CLICK)
In addition, we have two “Engineer It” video’s on basic DAC topics - one on MDACs and one on choosing Precision DACs. We have 4 more videos on the way, including videos about transient signals in industrial applications and how to design protection circuits for these transients. (CLICK)
Finally, we have three other presentations similar to this “MDAC Essentials” presentation. The first one “Precision DAC Essentials” focuses on introduces DAC specifications and the other two expand into the “soon to be released” 4-20 mA DACs with some additional depth into Industrial control system specifications.

## Slide 32: Questions? Email: k-duke@ti.com
Notes: 32